## Slide 1
Impact Assessment of Woodfuels Consumption on Deforestation and Forest Degradation in Cambodia
Himawari Hotel, 3 September 2015

## Slide 2: Outline
Understanding key terms and data
Introduction: Importance of woodfuels
Study Objectives
National woodfuels demand
Impact of woodfuels
Discussion
Simulation of strategic planning

## Slide 3: Some definitions
Woodfuels = firewood/fuelwood + charcoal
  1 kg of charcoal requires 6.4 kg wood
  1 kg of charcoal has 3 times the amount of energy of 1 kg firewood
Above ground biomass (AGB) is living biomass, total quantity or weight of plant organisms derived from trees in a given area, above the soil, generally refers to the trees, including branches, twigs, foliage, and stump.
Mean Annual Increment (MAI) is the average annual growth of the AGB.

## Slide 4
Results of 3 years of researches from GERES

## Slide 5: The importance of woodfuels in the energy mix
Chart: Total final energy consumption in Cambodia, in 2012 (Source: IEA)
| Oil products | Biomass energy | Electricity
 | 48022.596 | 139169.232 | 10885.68
Chart: Final biomass energy consumption in Cambodia, in 2013 (The FloWood project, GERES 2014)
| Firewood | Rice husk | Sawdust | Leaves | Charcoal
 | 44131.2874 | 4403.5466 | 228.0994 | 78.7531 | 9618.6003

## Slide 6: Woodfuels remain important regardless of wealth
GERES survey from 1,969 households, representative of the Cambodian population, shows that the share of households that use charcoal as a primary fuel does not decrease with an increase in wealth.
Chart: 
| Poorest | Poor | Better off
Electricity | 0 | 18436 | 21747
LPG | 12420 | 241262 | 147883
Charcoal | 71320 | 339507 | 134959
Wood | 278903 | 1447209 | 267171

## Slide 7: Currently woodfuels use is highly inefficient

## Slide 8: Study Objectives

## Slide 9: Study objectives
To determine the share of woodfuels which is sourced from forest and non-forest land in Cambodia; and
To assess the impact of woodfuels consumption on deforestation and forest degradation.

## Slide 10: National demand of woodfuels

## Slide 11: Annual woodfuels demand in Cambodia
1,300,000 tonnes of firewood collected locally for cooking

## Slide 12: Annual woodfuels demand in Cambodia

## Slide 13
440,000 tonnes of firewood bought for cooking
Annual woodfuels demand in Cambodia

## Slide 14: Annual woodfuels demand in Cambodia

## Slide 15: Annual woodfuels demand in Cambodia
3,000,000 tonnes of wood cut for charcoal production
Notes: ធ្យូងដែលផលិតបានគឺផ្គត់ផ្គង់ឲតែតម្រូវការតាមផ្ទះប៉ុណ្ណោះ។

## Slide 16: Annual woodfuels demand in Cambodia

## Slide 17: Annual woodfuels demand in Cambodia
780,000 tonnes cut annually for industrial activities

## Slide 18: Annual woodfuels demand in Cambodia

## Slide 19: Annual woodfuels demand in Cambodia
5,500,000 tonnes of wood cut for woodfuels consumption

## Slide 20: Impact of woodfuels on forest

## Slide 21: Pressure of wood collected by end-users over forest and non-forest
11% of wood is collected from forest by wood consumers
Notes: Place where wood is collected and quantity of wood which is collected by villagers/wood consumers

## Slide 22: Pressure of charcoal and purchased firewood over forest
Charcoal is responsible for 62% of the pressure of commercial woodfuels
Notes: Woodshed = កន្លែងដែលមានសក្តានុពលក្នុងការផ្តល់ឈើសម្រាប់ធើ្វជាធ្យូង និងឈើសម្រាប់លក់ឲ្យរោងចក្រ សហគ្រាសនានា​ នៅទូទាំងប្រទេស

## Slide 23: Annual woodfuels pressure on forests
3,400,000 tonnes of woodfuels are originated from forest, 73%
Notes: សរុបបរិមាណាឈើដែលដកហូតពីព្រៃ (ឈើប្រមូលដោយប្រជាជនសម្រាប់ប្រើប្រាស់ក្នុងផ្ទះ ឈើសម្រាប់ធ្វើធ្យូង ធ្វើអុសលក់ឲ្យរោងចក្រសហគ្រាស) មានចំនួន ៣.៤​លាន​តោន ឬស្នើរនឹង ៧៣%នៃតម្រូវការអុសធ្យូងនៅទូទាំងប្រទេស

## Slide 24: Forest degradation areas from national woodfuels consumption
380,000 tonnes of woodfuels exceeding from the supply
Notes: 38 ម៉ឺនតោន ជាបរិមាណជីវម៉ាស់ដែលដកហូតលើសប្រមាណ គឺលើសពីអ្វីដែលព្រៃអាចផ្តល់ឲ្យបាន ដូច្នេះវាត្រូវបានចាត់ទុកថាជាជីវម៉ាស់ដែលមិនកើតឡើងវិញ

## Slide 25: Forest degradation areas from Phnom Penh consumption
50% of total over-harvested amount is due to the demand from Phnom Penh

## Slide 26: Total Non-Renewable woodfuels consumption
1,200,000 tonnes of woodfuels biomass is not sustainable

## Slide 27: Currently the majority of non-renewable woodfuels is supply forest-to-agriculture land conversion
Chart: ktonnes
| Collected demand | Commercial demand | Collected demand | Commercial demand
NRB | 24.697 | 354.881 | 30.5262 | 775.5115
CO2 emission | 43.1506 | 620.0481 | 53.3353 | 1354.9737
32%
68%
Woodfuels exceeding from the supply
Woodfuels from forest-to-agriculture land conversion

## Slide 28
‘So what will happen when conversion of forests to agricultural land will no longer supply the woodfuels demand?’

## Slide 29: Over-harvested hotspot without the supply from deforestation
1,800,000 tonnes of NRB and 49% found inside protected areas

## Slide 30: Strategies to tackle woodfuels pressure
  Increase energy efficiency with:
  Improved cookstove for households
  Energy efficient technologies for industries
  Improved charcoal kiln for charcoal producers
  Increase the amount of supply via:
  Sustainable forest management in Community Forestry;
  Afforestation/reforestation using short-rotation plantations (Acacia, Bamboo…)
  Agro-forestry practices;
  Energy substitution:
  Agriculture by products - rice husk, coconut shells, corn cobs, cane sugar residues, peanut shells, saw dusk.
  LPG, Biogas, Solar

## Slide 31: Simulation of strategic planning to reduce NRB
Chart: 
Initial Deficit | 1790.758
Final Least Deficit | 1790.758
Example of Current Situation | Action/Project | Possible Result
1. Improved cookstove efficiency/ជំរុញឲ្យមានការប្រើប្រាស់ចង្ក្រានប្រណិតតាមគ្រួសារ |  | 
Current number of HH using charcoal stoves (numbers) | Share of HH switching to energy efficient technologies (KhROS: - 20%) | Wood saved (t/year)
1,000,000 |  | -
2. Energy efficiency for Industry/MSMEs / ជំរុញឲ្យមានការប្រើប្រាស់បច្ចេកទេសដែលសន្សំសំចៃថាមពលតាមរោងចក្រ ឬសហគ្រាសដែលប្រើប្រាស់ជីវម៉ាស់សម្រាប់ផ្គត់ផ្គត់ថាមពល |  | 
Current wood consumptions for industry activities (t/year) | Share of industries switching to energy efficient technologies (Average: - 20%) | Wood saved (t/year)
780,000 |  | -
3. Charcoal kiln efficiency / ជំរុញឲ្យមានការប្រើប្រាស់ឡធ្យូងប្រណិតតាមកន្លែងផលិតធ្យូងបុរាណ |  | 
Current wood consumptions for traditional charcoal production (t/year) | Share of traditional charcoal producers switching to energy efficient technologies (Improved Charcoal kilns: -20 %) | Wood saved (t/year)
3,000,000 |  | -
4. Energy substitution -> Ex: Ricehusk Briquette / ជំរុញឲ្យមានការប្រើប្រាស់ថាមពលជំនួស ឧ. ដុំធ្យូងអនាម័យធ្វើពីអង្កាម |  | 
Current ricehusk briquette product (t/year) | Quantity increase (t/year) | Wood saved (t/year)
10,000 |  | -
5. Increasing potential supply / ពង្រីកសក្តានុពលនៃការផ្គត់ផ្គង់ ផ្តោតសំខាន់លើតំបន់ជាប្រភពសម្រាប់អុស ធ្យូង |  | 
Current community forestry area (ha) | Increase in Community Forestry areas with Enrichment planting/Assisted Natural Regeneration (%) | Annual supply increase (t/year)
300,000 |  | -
Notes: Improved cookstoves : KhROS = khmer rocket stove

## Slide 32
Vannareth Huoy (Ms.)
v.huoy@geres.eu
Thank You
Website: http://www.geres.eu